## Slide 1
Data Fusion Fault-Tolerant Strategy for a Quadrotor UAV
TEAM CD-1
SARADHI-CB.SC.U4AIE24265
SATHVIK-CB.SC.U4AIE24240
ARYAN-CB.SC.U4AIE24341
DASARI RISHIKESH-CB.SC.U4AIE24365

## Slide 2
01 / INTRODUCTION — UAV Fault-Tolerant Navigation
• UAVs are used for surveillance, delivery, inspection and defense.
• A quadrotor has 4 motors but must control 6 degrees of freedom.
• So, correct position and movement information is very important.
• GPS → X and Y position.
• Lidar / Barometer → altitude (Z).
• IMU → acceleration and angular motion.
• Magnetometer → heading (yaw).
• If sensor information becomes wrong, the drone can become unstable.
• Our system also checks for hidden software faults in the estimator.
Data Fusion Fault-Tolerant UAV | 02

## Slide 3
02 / PROBLEM STATEMENT —
• GPS can suddenly show a wrong position, for example a +5 m jump.
• This wrong position can make the drone move or tilt incorrectly.
• Lidar can have a −1 m height bias and may cause unsafe altitude control.
• IMU measurements can become noisy because of motor vibration.
• A more difficult problem is an internal software fault.
• The Kalman filter covariance can become invalid or negative.
• Example: Pz = −0.1 or Pxy = −0.01.
• The physical sensors may still look healthy, so a normal sensor voter may not detect it.
• Wind and rain can make fault detection harder.
Data Fusion Fault-Tolerant UAV | 03

## Slide 4
03 / OBJECTIVES — What We Want to Achieve
• Reproduce the main results of the Hamadi et al. (2022) reference work.
• Use four sensor blocks as the input to the estimation system.
• Use two EKFs so that one estimator can act as a backup.
• Build an analytical dynamic model of the quadrotor.
• Use a weighted voting method to select a reliable state estimate.
• Detect both physical sensor faults and software estimation faults.
• Automatically isolate the faulty part and recover the drone.
• Create a realistic 3D MuJoCo airfield with wind and rain.
• Test takeoff, flight, fault injection and landing.
Data Fusion Fault-Tolerant UAV | 04

## Slide 5
04 / FULL PIPELINE — How Our Project Works
• Step 1: Sensor blocks provide measurements from the simulated drone.
• Step 2: Measurements are processed by EKF 1 and EKF 2.
• Step 3: Motor commands are also used by the analytical Dynamic Model.
• Step 4: The three estimates are compared by the weighted voter.
• Step 5: The voter produces one reliable consensus state.
• Step 6: FDI checks sensor residuals and estimator covariance.
• Step 7: If a fault is found, the faulty source is isolated.
• Step 8: A recovery solution creates a safe state estimate.
• Step 9: The recovered state goes to the PD controller.
• Step 10: The controller sends motor commands back to the MuJoCo drone.
• Easy flow: Sensors → Estimation → Voting → Fault Detection → Recovery → Control → Drone
Data Fusion Fault-Tolerant UAV | 05

## Slide 6
05 / METHODOLOGY — Mathematical Models & Estimators
• Motor input is converted into thrust and torque using fitted equations.
Thrust equation:
Fi = −1.4736u³ + 11.0691u² − 16.7074u + 7.3007 N
Torque equation:
τi = −0.0905u³ + 0.4771u² − 0.6790u + 0.3045 N·m
• The Dynamic Model describes the drone's 6-DOF motion.
• 6-DOF means X, Y, Z movement plus roll, pitch and yaw.
• The equations are solved using RK4 at 200 Hz.
• The Dynamic Model predicts motion using physics and motor inputs.
• EKF 1 is the primary state estimator; EKF 2 is the redundant backup estimator.
Joseph-form covariance update:
Pk = (I − KkHk)Pk|k−1(I − KkHk)ᵀ + KkRkKkᵀ
Data Fusion Fault-Tolerant UAV | 06

## Slide 7
05 / METHODOLOGY —
• The three branches give estimates of the drone state.
• We compare how close the estimates are to each other.
Similarity score:
sij = 1 / [1 + (dij / a)ⁿ]
• More consistent estimates receive higher weights.
Weight calculation:
wi = (Σj≠i sij) / (Σk Σj≠k skj)
Final voted state:
yvoted = Σ wi yi
• FDI means Fault Detection and Isolation.
GPS threshold: ΔGPS ≤ 2.0 m.
Lidar threshold: ΔLidar ≤ 1.0 m.
Software fault: min(diag(PKF1)) < 0.
Recovery 3: KF3 = ½(KF2 + DM).
Data Fusion Fault-Tolerant UAV | 07

## Slide 8
06 / SIMULATION — 3D MuJoCo Environment
• We created a realistic 3D airfield for testing the drone.
• The environment has a 60 m runway with center markings.
• It also contains a helipad, hangars, tower, radar dome and trees.
• The Tarot 650 drone performs its flight inside this environment.
• Wind turbulence is varied between about 4.0 and 6.5 m/s.
• Animated rain is also added to make the environment more realistic.
• A simple HUD shows position, altitude, wind and sensor residuals.
• The fault and consensus status can be monitored during flight.
• The HUD is placed in the corners so it does not block the main view.
Data Fusion Fault-Tolerant UAV | 08

## Slide 9
06 / SIMULATION —
• Situation 1 — GPS fault at t = 7 s.
• GPS receives a +5 m position error.
• The fault is detected quickly and the faulty estimator is isolated.
• The drone continues the runway circuit safely.
• Situation 2 — Lidar fault at t = 17.8 s.
• Lidar receives a −1 m height bias.
• The system maintains the drone near 3 m altitude.
• Situation 3 — software altitude fault: Pz = −0.1.
• The covariance health check detects the problem and disconnects KF1.
• Situation 4 — software position fault: Pxy = −0.01.
• The system uses KF3 from EKF 2 and the Dynamic Model.
• The drone continues its planned U-shaped path.
Data Fusion Fault-Tolerant UAV | 09

## Slide 10
07 / FUTURE WORK —
• Test the algorithms on real drone hardware.
• Port the system to PX4 and Pixhawk 6X.
• Implement the algorithms in C++.
• Test dual CAN-bus communication at 200 Hz.
• Perform outdoor tests under real wind and weather.
• Use LSTM or Transformer models to predict sensor degradation.
• Use NMPC to improve control during strong wind.
• Add rotor-failure handling for hexacopters and octocopters.
• Extend the voter to multiple drones.
• Allow healthy drones to share information with degraded drones.
Data Fusion Fault-Tolerant UAV | 10

## Slide 11
08 / CONCLUSION —
• We developed a fault-tolerant navigation system for a quadrotor.
• The system can handle both sensor faults and software estimator faults.
• Two EKFs provide redundant state estimates.
• The Dynamic Model provides an additional physics-based estimate.
• The weighted voter selects a reliable consensus state.
• FDI detects sensor errors and hidden covariance problems.
• Recovery methods allow the drone to continue flying after a fault.
• The system was tested in a 3D MuJoCo environment.
• GPS, Lidar and software faults were successfully tested.
• Wind and rain were also included in the simulation.
• Final idea: Sense → Estimate → Compare → Detect → Recover → Control → Fly safely.
Data Fusion Fault-Tolerant UAV | 11